## Slide 1
Priority Based Task Scheduler
Team Members : Guhan (Mtech ESE 22410) , Sai Krishna (Mtech ESE 23065)
Project Idea And Objectives
  Aim is to implement a priority based task scheduler using TIVA uC.
  We have a list of tasks with varying priorities. Currently, four tasks have been implemented.
  Each task corresponds to an infinite while(1) loop.
  As the task is running, we switch from one task to the next using pre-emptive scheduling.
  Pre-Emptive scheduling is the type of scheduling in which the OS decides when we need to switch from one task to the next.
  In this mini project, the Systick_Handler() function is called periodically and when this function is called , we switch the context and move from one task to the next.
  When priorities are considered, the task with the highest priority is performed more number of times when compared with tasks that have lesser priority.
  One of the ways in which we can make this more apparent is by having sine or cosine wave generation as one of the tasks.
  When this task is performed frequently, we get a smooth sine wave. When this task is performed less frequently, we get a distorted waveform.

## Slide 2: Block Diagram
Task 1
Task 2
Task 2
Task 3
Scheduler(Systick_Handler)
Here the colour of the arrows indicate the direction of control flow as we switch from one task to the next

## Slide 3: Progress
Four tasks have been implemented as infinite while(1) loops.
Varying priorities have been assigned to the tasks. Lower the number, higher the priority.
Each task has its own dummy stack to store its context as we move from the one task to the next.
The Systick_Handler() function has been configured to perform the task switching activity. Context of one task is saved by popping the contents from the TIVA registers on to the dummy stack of the particular task that is about to be suspended.
And when we move to the next task, contents from the dummy stack of the task that is about to be performed is loaded on the TIVA registers and execution of the next task takes place.
As of now, the tasks that have been executed involved only blinking of LEDs and concurrently displaying numbers on the Seven Segment Display of the Edu Arm Board.
Task with higher priority is allotted more CPU time than the tasks with relatively lower priority.
But the lower priority tasks are also performed for some time in order to avoid starvation.
Going forward, we aim to implement generating a sinusoidal waveform as one of the tasks and we hope to get a smooth waveform if this task is performed frequently and we hope to get a distorted waveform if this task is performed less frequently.